## Slide 1: TAU 2021 Timing Contest
Graduate Institute of Electronics Engineering
Department of Electrical Engineering
National Taiwan University
iTimer Team

## Slide 2: Team Members
Zi-Sheng Lin
Pei-Huan Tsai
Yu-Kang Lin
Shih-Kai Lee

## Slide 3: Advisors
Pei-Yu Lee
Iris Hui-Ru Jiang

## Slide 4: Our Framework
TICER based RC Reduction Algorithm
RC Network Reduction
Stage Delay Calculator
Y-parameter Extraction
Gate Delay/Slew Calculation
Driver Waveform Solving
Driver Waveform Reduction
Net Delay/Slew Calculation
Receiver Waveform Solving

## Slide 5: RC Network Reduction
TICER based RC Reduction Algorithm
RC Network Reduction
Stage Delay Calculator
Y-parameter Extraction
Gate Delay/Slew Calculation
Driver Waveform Solving
Driver Waveform Reduction
Net Delay/Slew Calculation
Receiver Waveform Solving

## Slide 6: RC Reduction Algorithm
Size of network is critical to both efficiency and stability
  Modify the TICER* algorithm for better accuracy when using CCS models
  Achieve 2.87x speed up in total runtime
(a) Original tree circuit
(b) Reduced circuit
*B. N. Sheehan, "TICER: Realizable reduction of extracted RC circuits," 1999 IEEE/ACM International Conference on Computer-Aided Design.
reduction
RMS error
in open testsuites

## Slide 7: Gate Delay/Slew Calculation
TICER based RC Reduction Algorithm
RC Network Reduction
Stage Delay Calculator
Y-parameter Extraction
Gate Delay/Slew Calculation
Driver Waveform Solving
Driver Waveform Reduction
Net Delay/Slew Calculation
Receiver Waveform Solving

## Slide 8: Solving Driver Waveform
Solve complete driver waveform instead of a single cell slew
  Attain accurate net delay/slew in Long Tail situation
Apply Multiple Voltage Threshold Model* (MVTM) algorithm
  Avoid interpolation in the time-axis
  Efficiently extract Y-parameters from RC trees
interconnect tree
CCS driver
CCS receivers
*P. Feldmann et. al., "Driver waveform computation for timing analysis with multiple voltage threshold driver models," 45th Design Automation Conference, 2008.

## Slide 9: Net Delay/Slew Calculation
TICER based RC Reduction Algorithm
RC Network Reduction
Stage Delay Calculator
Y-parameter Extraction
Gate Delay/Slew Calculation
Driver Waveform Solving
Driver Waveform Reduction
Net Delay/Slew Calculation
Receiver Waveform Solving

## Slide 10: Solving Receiver Waveform
Apply circuit simulation to solve receiver waveforms
  No extra Model-Order-Reduction applied since we have reduced the RC network
Driver waveform reduction
  33% runtime reduction to the circuit simulation in average
reduced waveform
receiver waveform
driver waveform
9 segments
5 segments

## Slide 11: Experimental Results
Correlation against SPICE simulation
  Achieve 0.998+ correlation in cell/net delay/slew.
Multi-threading performance
  8.3x speed up when using 16 threads
(a) Cell Delay
(b) Cell Slew
(c) Net Delay
(d) Net Slew

## Slide 12: Teamwork
TICER based RC Reduction Algorithm
RC Network Reduction
Stage Delay Calculator
Y-parameter Extraction
Gate Delay/Slew Calculation
Driver Waveform Solving
Driver Waveform Reduction
Net Delay/Slew Calculation
Receiver Waveform Solving
Zi-Sheng Lin
Yu-Kang Lin
Pei-Huan Tsai
INTEGRATION & TESTING
Shih-Kai Lee

## Slide 13
Thank You!